## Slide 2: Update on Design Progress
Obtained Survey, Geotech, and utility survey
Coordinating with Utility Owners
Coordinated with US Coast Guard
Developing Construction phasing
Hydraulic Modeling Completed
Held Kickoff meeting with City Staff
Working Towards the Initial Submittal

## Slide 3: Initial Design Highlights
Sample Road
  US Coast Guard Permitting will not be required
  Designed bridge Vertical Geometry to meet ADA without reducing clearance below
NE 31st Court
  Design to avoid impacts to Sanitary Lift Station
Both bridges
  Designing to avoid impacts to adjacent seawalls

## Slide 4: City Input – Barrier Separated VS Raised Sidewalk
Barrier Separated Sidewalk
(Lighthouse Drive)
Raised Sidewalk
(SE 5th Avenue – City of Pompano Beach)

## Slide 5: Barrier Separated
Existing Bridge Drainage
Overhead Utilities
Stormwater Discharge
Pros
  Provides pedestrians physical separation from vehicles
Cons
  End Transitions require guardrail
    Sub-standard guardrail
  FDOT getting away from Barrier Sloped End treatments
  Provides less opportunity for gateway feature
  Requires wider bridge and second railing system
    ~$20k more as compared to raised sidewalk
  More costly long-term maintenance

## Slide 6: Barrier Separated - Sample Road layout
Existing Bridge Drainage
Overhead Utilities
Stormwater Discharge
Utilities and Permitting
Typically seen on higher speed roads
Requires substandard guardrail
Provides less opportunity for gateway feature
Bike Lane
Bike Lane
Sidewalk

## Slide 7: Barrier Separated – Example Pictures
Existing Bridge Drainage
Overhead Utilities
Stormwater Discharge
Atlantic Avenue (Delray Beach)
Hood Road over I-95 (West Palm Beach)

## Slide 8: Raised Sidewalk
Existing Bridge Drainage
Stormwater Discharge
Pros
  Simplified End Transitions
    Flare out the Barrier walls
    Guardrail not required
  Provides more opportunity for gateway features
  Narrower bridge with one railing
    ~$20k less as compared to barrier separated
  Lower long-term maintenance cost
    No Guardrail
Cons
  Does not provide pedestrians with physical separation from vehicles

## Slide 9: Raised Sidewalk – Sample Road layout
Existing Bridge Drainage
Stormwater Discharge
Utilities and Permitting
Bike Lane
Bike Lane
Sidewalk
Typically seen on low speed residential
Guardrail not required for transition
Provides opportunity for gateway feature

## Slide 10: Raised Sidewalk – Example Pictures
Stormwater Discharge
Gordy Road (Saint Lucie County)
Terra Mar Drive over Spanish River (Pompano Beach)

## Slide 11: Raised Sidewalk – Gateway Feature
Stormwater Discharge
SE 5th Avenue over Pompano Canal (Pompano Beach)

## Slide 12: City Input - Traffic Railing Options
Standard FDOT Traffic Railing (Lighthouse Drive)
Both Railings are Crash Tested
Aesthetic Texas Traffic Railing
(Charlotte County)

## Slide 13: Traffic Railing Options – Aesthetic Railing
NE 24th Avenue Bridge Considerations
Standard Texas Traffic Railing (Chamberlain Blvd)
Railing is Crash Tested
~ $30k Increase as compared to FDOT Railing

## Slide 14: Questions?
14
Requested Input from Commission
  Barrier Separated vs Raised Sidewalk
  FDOT Railing vs Texas Railing